## Slide 1
Working Principle of PV Combiner Box
Technical Analysis and Application
Notes: Hello everyone, today I will explain in detail the working principle of the PV combiner box. This PPT will comprehensively introduce this key device in the photovoltaic system from definition, structure, principle to application.

## Slide 2
Table of Contents
1. What is a PV Combiner Box?
Understand the basic definition, core functions, and industry standards of a PV combiner box.
2. Core Structure and Components
Deep dive into internal core components, such as fuses, surge protectors, and monitoring modules.
3. In-depth Analysis of Working Principle
Detailed breakdown of the entire process of power combination and signal acquisition through a flowchart.
4. Application Scenarios and Value
Explore the practical applications and value in large-scale PV power plants and distributed generation.
Notes: This presentation will be divided into four parts. First, we will understand the basic definition and function of the PV combiner box; second, we will delve into its interior to see what core components it consists of; then, we will analyze its working principle in detail through a flowchart; finally, we will discuss its practical application scenarios and core value.

## Slide 3
Definition and Core Functions
What is a PV Combiner Box?
A PV Combiner Box, also known as a PV DC Combiner Box, is a core transfer device on the DC side of a photovoltaic power station, responsible for centralizing the power from PV strings.
Combining: Centralized Power Transmission
Aggregates DC power from multiple PV strings, effectively reducing cable quantity and cost while improving transmission efficiency.
Protection: Safety Guardian
Provides multiple protections such as short circuit, overcurrent, reverse connection, and lightning strike protection to ensure system safety.
Monitoring: Smart O&M
Smart combiner boxes monitor the operating parameters of each string in real-time, enabling quick fault location and significantly reducing O&M difficulty.
Notes: 简单来说，光伏汇流箱就是光伏电站里一个负责“中转”和“安保”的关键角色。它的主要工作是把很多组光伏板发出来的电汇集到一起，同时像一个保安一样，提供各种保护功能，并在智能版本中，实时监控每一路的运行状态，让我们能清楚地知道系统是否健康。

## Slide 4
Core Structure Breakdown
Enclosure
Provides outdoor protection (IP65), corrosion-resistant.
String Protection
Each string is equipped with a DC fuse (short circuit protection) and a reverse diode (prevents current backflow).
Main Switch
PV-specific DC circuit breaker for disconnecting the combiner box from the inverter.
Surge Protection Device (SPD)
Discharges surge energy to protect equipment.
Notes: This diagram shows the typical internal structure of a combiner box. From the outside in, a sturdy enclosure provides protection; each input string is protected by a fuse and a reverse diode; after the electricity from all strings is combined, it is output through a main circuit breaker; at the same time, the surge protection module and smart monitoring unit ensure the safety and intelligent operation of the system.

## Slide 5
Working Principle Flowchart
01 Power Generation
PV strings generate DC power
02 Input
Multiple DC power sources enter the combiner box separately
03 String Protection
Each string undergoes overcurrent and reverse connection protection
04 Combining
The currents of all normal strings are combined in parallel
05 Main Output
The combined large current is output to the inverter
06 Safety Protection
Surge protection module provides real-time protection
07 Smart Monitoring
Collects various data and uploads it
Notes: The working process of the combiner box can be summarized in these seven steps: After the solar panels generate electricity, the current enters the combiner box, undergoes fine protection for each string, then all healthy currents are combined to form a powerful current output to the inverter. Throughout the process, lightning protection and smart monitoring are always online, ensuring the safety and stability of the system.

## Slide 6
Application Scenarios and Core Values
Main Application Scenarios
Large-scale ground-mounted PV power plants
Commercial and industrial rooftop PV projects
Distributed PV systems
Core Values
Simplified Wiring
Reduces cable quantity, lowering construction and material costs.
Enhanced Safety
Multiple protection mechanisms effectively avoid electrical risks.
Easy O&M
Real-time data monitoring enables refined management and quick fault response.
Notes: Combiner boxes are widely used in photovoltaic projects of all scales, from large ground-mounted power plants to commercial and industrial rooftops, and distributed systems. Its core values are reflected in three aspects: it greatly simplifies on-site wiring, significantly improves the safety level of the system, and through intelligent monitoring, makes the operation and maintenance of the photovoltaic system more efficient and convenient than ever before.